## Slide 1
Obafemi Awolowo University(Electronic and Electrical Engineering)
Ogundeji Abiola Samuel (EEG/2018/114)
NON INTRUSIVE LOAD MONITORING
INTRODUCTION
to develop a non-intrusive system to track the consumption of individual loads for consumers.
to furnish consumers with detailed information on appliance usage.
to create a system aimed at decreasing and conserving electrical energy in residential structures.
to promote energy efficiency, reduce consumption patterns, and enable efficient demand-side management through system development.
PROBLEM STATEMENT
Global fossil fuel consumption impacts climate change.
Household energy use comprises over 30% of total energy consumption.
Research shows effective feedback of energy usage can save up to 20% .
ILM energy monitoring methods are costly.
There is a need for affordable, non-intrusive load monitoring.
The measuring module takes the total electrical power reading from the main power board. The microcontroller with wifi capability, saves the electrical data on the SD-Card. The RTC module adds the time stamp to the collected data. The saved data is now sent to the database for further processing.
BLOCK DIAGRAM
This Study focuses on Non-intrusive Load Monitoring (NILM) for household energy management
NILM involves analysis of energy usage without direct appliance interference
This approach provides robust and efficient solution for energy monitoring
METHODOLOGY
EXPERIMENTAL
SET-UP
ILM and NILM
Data Acquisition: Low frequency or High Frequency Sampling
Feature Extraction: Steady state signature and Transient state signature
Appliance Classification: Supervised and Unsupervised machine learning, using Neural Networks
CURRENT WORK
CONCLUSION
Research indicates that providing users with feedback on their appliances’ energy consumption can lead to a 20% reduction in household energy consumption.
This reduction in energy consumption helps to mitigate climate change caused by the consumption of fossil fuels by electrical generators.
The study aims to develop a non-intrusive method for monitoring individual appliance energy consumption.
However, as the study is ongoing, results are not yet available.
FUTURE WORK
I am working on integrating the data acquisition components.
I am also in the process of writing an Arduino Sketch to handle data processing and transmission to the database.
I plan to carry out feature extraction and appliance classification.
FIGURE 1: Global Fossil Fuel Consumption
FIGURE 4: Breadboard Implementation of Data Acquisition
FIGURE 3: Block Diagram of the NILM System
FIGURE 2: Installation of Sensor(s) between NILM vs ILM